## Slide 1: Automating the rainwater regulation
Simon Baecke
02/03/2023

## Slide 2: Rainwater regulation
2 parallel regulations
  Building scale
  Plot scale
Data from 3 data sources
  BIM
  GIS
  Conceptual idea

## Slide 7: BPMN,DMN & CMMN
Source: Object Management Group

## Slide 8: BPMN

## Slide 9: CMMN

## Slide 10: DMN

## Slide 12: BPMN2.0 XML
BPMN is based on the XML schema
5 types of objects
  Events
  Tasks

## Slide 13: BPMN2.0 XML
  Gateways
  Artifacts
  Connections

## Slide 17: Proof of concept
Data in .csv file
  Plot area > 250m²
  Not in water extraction area so infiltration

## Slide 18: Reflection
Include part 1 of rainwater regulation
Extract data from sources (when needed)
Implement in BIM software to send warnings
Web page with file upload
Output format

## Slide 19: GIS data
Extract coordinates from address (and vice versa)
  Geolocation Service API by Digitaal Vlaanderen
  Data van CRAB, Urb-IS & POI
Extract area of plot and location of water extraction areas
  WFS open data

## Slide 21: WFS
Grootschalig Referentiebestand (GRB)
  Hosted by Digitaal Vlaanderen
Grondwaterwingebieden en beschermingszones (2016)
  Hosted by Databank Ondergrond Vlaanderen

## Slide 23: BIM data
Roof type
Building type
Building area
Horizontal projected roof area (old & new)
Pavement area (old & new)
Foreseen infiltration area

## Slide 24: BIM data hurdles
No general way to indicate if building type is a single-family dwelling
Sites are not always modelled in BIM environment
Projected horizontal area of site can be complex
Modeling differences:
  Area of the roof
  Site